## Slide 1
Hardware Reverse-engineering Tools new threats – new opportunities
Texplained

## Slide 2
8 years in a security lab
Technology lover
Analysis techniques // exploits
Involved from sample preparation to report writing
  Optical systems setup
  Sample preparation
  Delayering
  Imagery
  Software developments
Bio
Texplained

## Slide 3
Texplained
Semi-invasive attacks
Invasive attacks – circuit edit
Micro-probing
Various experiments
    Photoemission
    AFM techniques
    Electrical glitch
Bio

## Slide 4
Texplained
Focus on Hardware reverse engineering
Evolution of the all process
  Sample preparation
  Imaging
  Study
Change in evaluation criterias
Future evolutions
Talk Description
Talk description
context
HRT outcomes
HRTs as the next step
Future developments

## Slide 5
Texplained
Attacks summary
Chip classification
Context
context
HRTs as the next step
HRT outcomes
Future developments

## Slide 6
Texplained
Non invasive attacks - VCC and Clk glitch
Context – Attacks summary
Take advantage of the RTL technology
Used to skip instructions or to disturb the normal execution
Finding the glitch pattern is empirical
The real effect stays hidden

## Slide 7
Texplained
Semi-invasive attacks - Sample preparation techniques
Partial opening - frontside
Context – Attacks summary

## Slide 8
Texplained
Semi-invasive attacks - Sample preparation techniques
Repackaging
Context – Attacks summary

## Slide 9
Texplained
Semi-invasive attacks - Sample preparation techniques
In situ:
Context – Attacks summary

## Slide 10
Texplained
Semi-invasive attacks – Principle
1064 nm laser spot can induce transistor switch
Silicon is « transparent » @1064 nm
Metal planes prevent laser fault injection
Fault is injected at a precise given location
Context – Attacks summary

## Slide 11
Texplained
Semi-invasive attacks – Tests
Fishing :
. Unknown timing
. Vague localization
. Trial and Error
=> Working ;-)
Context – Attacks summary

## Slide 12
Texplained
Semi-invasive attacks – Tests
Automated fishing (a first step toward laser scan) :
. XY stages for chip positioning
. One position – several laser pulses
. Pass-fail from data returned by the device
. One scan per timing of interest
=> Different effects
Context – Attacks summary

## Slide 13
Texplained
Semi-invasive attacks – Tests
Targeted shot :
. Precise localization from laser scan image
. Timing still critical
Context – Attacks summary

## Slide 14
Texplained
Invasive attacks
Get access to the circuitry itself and apply modification for
Shield bypass
Embedded counter-measures deactivation
Data extraction
Context – Attacks summary

## Slide 15
Texplained
Invasive attacks
The process : delayering and imaging
Delayering requires skills and machinery
Optical and / or SEM scan
Pictures stitching is key
Alignment of layers must be precise
Context – Attacks summary

## Slide 16
Texplained
Context – Imaging techniques
Optical scans are fast to perform but :
Good tilt setup for high resolution scan is a nightmare (narrow depth of field)
Small features become invisible with technology size reduction
Oxide layers are light transparent (every deeper layer is visible)
Pictures lack information such as vias
Invasive attacks
The process : optical imaging

## Slide 17
Texplained
Context – Imaging techniques
SEM scan are slow (hours range) and pictures are distorted but :
Depth of field is bigger
Resolution is higher
Oxide layers are not transparent (one visible layer at a time)
Invasive attacks
The process : SEM imaging

## Slide 18
Texplained
Invasive attacks
The process : “Reverse-engineering”
Intensive use of pictures
Generate a test procedure
Localize points of interests
Context – Attacks summary

## Slide 19
Texplained
Invasive attacks
The process : Fib edit
Context – Attacks summary

## Slide 20
Texplained
Invasive attacks
The process : Micro-probing
Context – Attacks summary

## Slide 21
Texplained
Invasive attacks
Linear Code Extraction
Context – Attacks summary
2 major types of instructions : sequential / jumps
Provide only one instruction to the core of sequential type
Core will execute something useless
Address will be incremented
The entire code will be outputted from NVM memory
=> Most successful invasive attack

## Slide 22
Texplained
Invasive attacks
Linear Code Extraction
Context – Attacks summary
Cut and setup an instruction for the core (ex. nop)
Read data before the cut

## Slide 23
Texplained
Invasive attacks
Linear Code Extraction : Less FIBing – more options
Context – Attacks summary
Use buffer or register / latch signal to prevent read buffer output update
Read data before the buffer (register / latch)
Running code extraction is straight forward
Modification of the code is possible
Skipping instruction is possible (jumps…)

## Slide 24
Texplained
Context – Chip classification
3 different kind of security levels :
Weak : code can be extracted by old techniques or LCE
Adequate : old techniques do not work // LCE can be done at the costs of Hardware Reverse-engineering
Advanced : Hardware Reverse-engineering is mandatory for a code extraction + hardware functions have to be found and studied

## Slide 25
Texplained
Context – Chip classification
3 different kind of security levels :
Chip manufacturer | Pirates | Customer | 
Weak | Trivial | Dangerous cheap | No way
Adequate | Tricky | Balanced | Dangerous cheap
Advanced | Headache provider | Overkill expensive | Mandatory expensive

## Slide 26
Texplained
HRTs as the next step
HRT outcomes
Future developments
Hardware Reverse-engineering Tools the next step

## Slide 27
Texplained
HRTs as the next step
Analysis techniques evolution :
Laser fault injection
ROM code extraction
LCE
Other techniques
Sample preparation and imaging evolution :
Sample preparation
SEM imaging
Accurate correlation
All chip features become visible and usable

## Slide 28
Texplained
Usual tests target registers or memory output
Where are the working registers?
Is the memory encrypted?
Results can be achieved but hardly exploited
Fishing tests are also effective
Needed equipment price can be quite low
Effect can not be predicted
Timing and spot localization have to be found
Results can be achieved but can’t be fully understood therefore exploits are difficult to build
Fishing is a real threat
Analysis techniques evolution :
Laser fault injection
HRTs as the next step

## Slide 29
Texplained
Reading extra bytes from RAM while glitching during the ATR routine
Number of extra bytes depends on glitch location
Change mode of execution
Effect is “stored”
Original mode can be restored
Instruction skip
Registers can be found by fishing
Fault injected inside the core – what happened?
Analysis techniques evolution :
Laser fault injection : examples
HRTs as the next step

## Slide 30
Texplained
Principle does not change
Memory encryption
Multiplexers mixed with the core
Analysis techniques evolution :
LCE evolution
HRTs as the next step

## Slide 31
Texplained
Analysis techniques evolution :
LCE evolution : hidden mux
HRTs as the next step
8 bits processor
32 bits FLASH output going to the core

## Slide 32
Texplained
Analysis techniques evolution :
LCE evolution : hidden mux
HRTs as the next step
Lines have to be traced inside the core to find the 8 bits data bus.

## Slide 33
Texplained
Analysis techniques evolution :
LCE evolution : hidden mux
HRTs as the next step
3 paths can be followed :
2 of them can not be exploited

## Slide 34
Texplained
Analysis techniques evolution :
LCE evolution : hidden mux
HRTs as the next step
Finding the correct spot took some time
Multiplexers were hidden
Data was not encrypted

## Slide 35
Texplained
Analysis techniques evolution :
LCE evolution : state of the art
HRTs as the next step
Multiplexers are hidden
NVM content is scrambled
NVM content is encrypted
Hardware custom functions are implemented as part of the core
Several thousands gates have to be reversed

## Slide 36
Texplained
Analysis techniques evolution :
ROM reading : ROM “optical reading”
HRTs as the next step

## Slide 37
Texplained
Define 4 corners for alignment
Affine transformation to compensate “tilt deformation”
Define horizontal bit spacing
Define vertical bit spacing
Choose criteria for bit value
Extract defined zone
Analysis techniques evolution :
ROM reading : principle
HRTs as the next step
00100111
10101001
10001101
00011101
00001111
11100000
11111101
11111110
11010101
00011101
00001111
11100000
11111101
00011101
00001111
11100000

## Slide 38
Texplained
As ROMs are getting bigger, correlation errors have to be considered
Analysis techniques evolution :
ROM reading : correlation issue
HRTs as the next step
4700 pictures have to be stitched

## Slide 39
Texplained
Analysis techniques evolution :
ROM reading : correlation issue
HRTs as the next step
Smarter procedure :
Do not try correlating pictures (especially SEM pics) of a large scan
Do not try to tell your script where the bits are
Find bits corresponding to a noticeable value
Extract a grid from their position
From the grid, recover the missing bits
Correlate bits from an image with those of the adjacent one and so on

## Slide 40
Texplained
Sample preparation and imaging evolution :
Deprocessing :
HRTs as the next step
By using plasma etching as the only technique for deprocessing, picture quality is poor

## Slide 41
Texplained
Sample preparation and imaging evolution :
Deprocessing :
HRTs as the next step
Using combination of techniques such as Plasma etching, Chemical Mechanical Polishing and wet chemical etching leads to “perfect” deprocessing, suitable for SEM scan.

## Slide 42
Texplained
Sample preparation and imaging evolution :
Deprocessing :
HRTs as the next step
One layer visible at a time
Vias also visible
Custom process to distinguish vias and lines has been defined

## Slide 43
Texplained
Sample preparation and imaging evolution :
SEM imaging :
HRTs as the next step
Major issue was found and solved : SEM picture distortion
Tilt adjustment table has been machined
Fast scan
Distortion is calculated for a given scan and reversed

## Slide 44
Texplained
Sample preparation and imaging evolution :
Features on grid :
HRTs as the next step

## Slide 45
Texplained
Sample preparation and imaging evolution :
Find vias :
HRTs as the next step

## Slide 46
Texplained
Sample preparation and imaging evolution :
Find lines :
HRTs as the next step

## Slide 47
Texplained
Sample preparation and imaging evolution :
Accurate correlation
HRTs as the next step
Correlation is performed on feature coordinates “grid pattern”
At worst, lines are “jittering” around the calculated grid position

## Slide 48
Texplained
Sample preparation and imaging evolution :
Accurate correlation
HRTs as the next step

## Slide 49
Texplained
Sample preparation and imaging evolution :
2 layers example:
HRTs as the next step

## Slide 50
Texplained
Sample preparation and imaging evolution :
All information available
HRTs as the next step
Vias and lines are extracted on a grid
Gates are detected from the same mechanics
No correlation error
Layers are aligned “perfectly” without further picture transformation
No more pixels – polygons only 

## Slide 51
Texplained
HRT outcomes
Future developments
Sample preparation and imaging evolution :
All information available
HRTs as the next step
Hardware Reverse-engineering Tools outcomes

## Slide 52
Texplained
New possibilities :
Some possible studies
HRTs’ outcomes
semi-invasive preparation
LCE preparation
Shield global bypass
Other embedded counter-measures bypass

## Slide 53
Texplained
New possibilities :
Other techniques
HRTs as the next step
Photoemission
EMA
Dynamic voltage contrast

## Slide 54
Texplained
New possibilities :
New tools
HRTs’ outcomes
FIB navigation files can be generated
Planarised chip
Backside edit

## Slide 55
Texplained
HRTs’ outcomes
Particular gates can be highlighted without any further study
Fire at the located registers and see the effects
Tracing signals is easy as a click
Fire first, with for example a pass-fail scan
Look at what you hit at “fail” location
Understand the effect
=> From laser glitching to laser fault injection.
New threats :
Laser fault injection :

## Slide 56
Texplained
Context – Attacks summary
New threats :
Laser fault injection become cheaper

## Slide 57
Texplained
Path chain are very easy to spot
Used to debug / program the device
HRTs’ outcomes
New threats :
Scan chains analysis :

## Slide 58
Texplained
Timing consideration :
Real world example :
HRTs’ outcomes
ROM chip
ROM is scrambled
Multiplexers are hidden inside the logic
ROM is encrypted
Data encryption based on address and hard-wired key
-> Clear data bus location ?
-> Custom encryption reverse ?

## Slide 59
Texplained
Timing consideration :
Image preparation : “manual process”
HRTs’ outcomes
Correlation is based on pixel value :
From 10 minutes to several hours
Errors are inevitable
Image stitching is not reliable
One picture = one photoshop layer
Local adjustments are performed when needed
Alignment of 2 layers almost unfeasible but fast
Local adjustments are performed when needed

## Slide 60
Texplained
Timing consideration :
Finding data bus : “manual process”
HRTs’ outcomes
Tons of layers are used and moved for local adjustment : Errors
A schematic must be drawn to avoid being lost : Errors + you will get lost anyway

## Slide 61
Texplained
Timing consideration :
Finding data bus : “manual process”
HRTs’ outcomes
Each found gate must be analyzed even if already studied : Errors + stay patient
Equations have to be written in “mathematical form” : Many errors
cell_3_12 = (cell_9_24 xor cell_9_18) xor cell_1_18
cell_3_13 = (cell_9_20 xor cell_9_19) xor cell_1_23
cell_3_13bis = (cell_3_14 xor cell_9_25) xor cell_5_2
cell_3_14 = (cell_8_4 xor cell_g_1) xor cell_6_7
cell_3_15 = (cell_alpha_1 xor cell_9_40) xor cell_13_6
cell_3_16 = (cell_a_1 xor cell_1_19) xor cell_13_3
cell_3_17 = (cell_9_21 xor cell_9_22) xor cell_1_24

## Slide 62
Texplained
Timing consideration :
Finding data bus : “manual process”
HRTs’ outcomes
-> Finally, with help of vhdl software (for example), schematic can be re-arranged to understand the functions.
  Localization of the clear data bus is possible
  LCE is working
-> My FIB is down but I have reverse-engineered every single gate, I can read the ROM…
  VHDL simulations will show…. that there are errors 
  Localizing the errors can partially be made from simulations
  Where are the last errors?

## Slide 63
Texplained
Timing consideration :
Deprocessing
HRTs’ outcomes
Deprocessing for hardware reverse-engineering takes extra steps
This process is not suited for optical imaging
Complete deprocess can be achieved in about a week

## Slide 64
Texplained
Timing consideration :
Image preparation : with HRT
HRTs’ outcomes
Select area of interest and selection of rejected features(10 minutes per layer)
Find vias (> 100 images per minutes)
Find grid and lines (< 1 hour per layer)
Extract gates (1 hour)
Correct one layer : (1 day)
Correlate and transform pictures + generates layer netlist (< 1 hour)
Align 2 layers together (2 minutes)

## Slide 65
Texplained
Timing consideration :
Reverse-engineering custom logic : with HRT
HRTs’ outcomes
One layer per layer
  No stitching problem
  No local layer adjustment
One click to follow net(s)
Equations are generated automatically as well as schematic
  No re-writing errors, software is highlighting what is missing

## Slide 66
Texplained
Timing consideration :
Timing :
HRTs’ outcomes
After 2-3 weeks, every features are detected with good HRT
2 weeks later (average), LCE can be started
Same work with « manual process » would take months

## Slide 67
Texplained
Timing consideration :
Timing difference : reversing custom logic
HRTs’ outcomes
6 months after start of the study, results are still not exploitable
With first generation of HRT, same study was performed in 2 months
With next generation of the tool, time will be reduced to 1 month
  * With classical method, you would not have found the correct spots for LCE at this stage

## Slide 68
Texplained
New threats : Possible “achievements” :
HRTs’ outcomes
100 % success rate for hackers (excluding customized chip)
6 to 12 microcontrollers a year (first extraction)
XX customized chip a year
The advanced security level becomes at best adequate
  Custom hardware functions become a new kind of ROM that could be extracted from pictures only
Piracy
Counterfeiting
Patent violation

## Slide 69
Texplained
New opportunities :
HRTs’ outcomes
Better security level : in depth security evaluation with new techniques
Design and routing new strategies to make invasive work more complicated
Anti-piracy by changing the nature of the hardware custom functions
Affordable patent violation studies
Counterfeiting characterization
ICs’ obsolescence

## Slide 70
Texplained
New opportunities :
HRTs’ outcomes
Future developments

## Slide 71
Texplained
Future developments
Schematic creation and interaction
From gates to functions : automatic gates grouping to reduce number of blocs to study
Fast detection of « non aligned » features : from core to chip
Simulator, specific analysis
…

## Slide 72
Texplained
Hardware Reverse-engineering Tools new threats – new opportunities
Q&A…
Olivier Thomas
+33 664 800 687
olivier@texplained.com
Notes: END
thank you for your attention
I would be very happy to answer to your questions.
thanks.